## Slide 1: Tow Mater 5SIEC 2022-2023 / By Team Benny
The aim of this project is to tow a damaged vehicle with an autonomous vehicle. The goal is to make safety our priority! The vehicle has to approach the damaged vehicle slowly, taking into account its environment. It has to detect and avoid obstacles on its way towards the damaged vehicle. Then it should park and maneuver to reach the towing device of the damaged car.
STUDENTS
Léonie Hatte - Imane El Khamlichi - Alexis Pierre Dit Lambert -Martin Cheliz - Samantha Gorrin-Ascanio - Laura Mendes
TUTORS
Sébastien Delautier - Didier Le Botlan
THE TOWING CAR STATE MACHINE
THE TOWING CAR ARCHITECTURE
Jetson Nano – ROS 2 Humble (Docker)
Raspberry Pi 3 – ROS 2 Humble
Nucléo F103RB
Nucléo
L476RG
Ethernet
CAN
MOTORS
US
IMU
GPS
CAMERA
LIDAR
HOOK
THE DEMONSTRATION
THE MANEUVER
THE AVOIDANCE OF OBSTACLES
Avoid through the side without obstacles
Go through the side where there is the most space
Avoid a small (≃ 10cm) or big (≃ 30cm) obstacle
Obstacles detected by the Ultrasonic Sensors
Obstacles detected by the LiDAR
Move backwards
Move forward
Without U-turn
(= directions)
With U-turn
(≠ directions)

## Slide 2
OUR FEATURES
THE TESTS
Safety distance of 15 cm during avoidance
Maximum 20 cm drift from its trajectory
Identify a fixed obstacle after 5s
Alignment of maximum 5 cm interval
Maximum 10 m gap
GPS coordinates +/- 50 cm
Maximum 10 s after receive the coordinates
Autonomous towing
Tow at least 2 meters on a straight line
Stops 75 cm +/- 5 cm away from obstacle
Detect the QR code at a distance between 20cm and 100cm
Maneuvering in a 5m radius
Avoids obstacles with a width of less than 30cm

## Slide 3: Tow Mater 5SIEC 2022-2023 / By Team Benny
The aim of this project is to tow a damaged vehicle with an autonomous vehicle. The goal is to make safety our priority! The vehicle has to approach the damaged vehicle slowly, taking into account its environment. It has to detect and avoid obstacles on its way towards the damaged vehicle. Then it should park and maneuver to reach the towing device of the damaged car.
STUDENTS
Léonie Hatte - Imane El Khamlichi - Alexis Pierre Dit Lambert -Martin Cheliz - Samantha Gorrin-Ascanio - Laura Mendes
TUTORS
Sébastien Delautier - Didier Le Botlan
THE TOWING CAR STATE MACHINE
THE TOWING CAR ARCHITECTURE
Jetson Nano – ROS 2 Humble (Docker)
Raspberry Pi 3 – ROS 2 Humble
Nucléo F103RB
Nucléo
L476RG
Ethernet
CAN
MOTORS
US
IMU
GPS
CAMERA
LIDAR
HOOK
THE DEMONSTRATION
THE MANEUVER
THE AVOIDANCE OF OBSTACLES
Avoid through the side without obstacles
Go through the side where there is the most space
Avoid a small (≃ 10cm) or big (≃ 30cm) obstacle
Obstacles detected by the Ultrasonic Sensors
Obstacles detected by the LiDAR
With U-turn: ≠ direction
Without U-turn: =direction

## Slide 4
OUR FEATURES
THE TESTS
Safety distance of 15 cm during avoidance
Maximum 20 cm drift from its trajectory
Identify a fixed obstacle after 5s
Alignment of maximum 5 cm interval
Maximum 10 m gap
GPS coordinates +/- 50 cm
Maximum 10 s after receive the coordinates
Autonomous towing
Tow at least 2 meters on a straight line
Stops 75 cm +/- 5 cm away from obstacle
Detect the QR code at a distance between 20cm and 100cm
Maneuvering in a 5m radius
Avoids obstacles with a width of less than 30cm