## Slide 1
Notes: LEONIE
Hello everyone, today we witnessed an accident: a damaged car lies on the middle of the road in a dangerous area. No mistakes are possible, and it is not possible to send any human operator. There are too many debris on the road, and we heard that a landslide could occur.
The only solution we have is to send a car from Tow Mater! No need to jeopardize any human life, every towing is autonomous and safe. Fortunately, we know that the GPS system of the damaged cars and their towing devices are not harmed.

## Slide 2: Tow Mater
Fourth review
+ Martin Chéliz
+ Laura Mendes
+ Samantha Gorrin
+ Alexis Pierre Dit Lambert
+ Imane El Khamlichi
+ Léonie Hatte
Notes: LEONIE

## Slide 3: Table of content
The final product
Release vision
Fourth release
Demonstration
Tests
Sprint evaluation
Time Schedule
Next Sprint
Demonstration
Tests
FMECA
Trajectory Fault Tree
Obstacle Fault Tree
Camera Fault Tree
Notes: LEONIE

## Slide 4: Part 1 : The product
Notes: LEONIE/IMANE

## Slide 5: The final product
1
Sending GPS coordinates and reaching the damaged car
2
Maneuvering to place the hooks face to face
3
Reversing and locking
4
Towing
Performing the alignment maneuver and towing the car
Detecting and avoiding obstacles
Communicating with damaged car
Reaching the damaged car
Notes: IMANE

## Slide 6: Release vision
  Follows a straight line
  Locks the hook
  Detects large obstacles
  Speed regulation
Sprint 1
  No U-turn
  Detects small obstacles
  Identifies the car
  Tows in a straight line
Sprint 2
  U-turn
  Identifies moving obstacles
  Stops when moving obstacles
Sprint 3
  Avoids fixed obstacles during alignment maneuver
  The vehicles communicate
Sprint 4
  Reaches the damaged car
  Performs the alignment
Sprint 5
Notes: MARTIN

## Slide 7: Fourth release
Get obstacle width and position with the Lidar
Detecting and avoiding obstacles
Higher Priority
Time
10/01
13/12
Lower Priority
Léonie
Alexis
Martin
20/12
Implement the avoidance trajectory
27/12
03/01
Samantha
Imane
Laura
8
13
Detecting small or big moving obstacles
3
Communicating with the damaged car
Send GPS coordinates to the towing vehicle
Configurate the communication between the two cars (send ACK)
Get the GPS coordinates of the damaged car
3
3
3
Alexis
Samantha
Notes: MARTIN

## Slide 8: Part 2 : The demo
Notes: MARTIN/LAURA

## Slide 9
Demonstration
Avoiding fixed obstacle
Getting an obstacle position
Sending GPS coordinates
Sending acknowledgement
Notes: LAURA
9

## Slide 10: Tests (1/2)
Sending GPS coordinates
GPS coordinates +/- 0,0001 °
(≈ 50cm)
Maximum 10m one from another
Maximum 10 s after receiving the coordinates
Sending acknowledgement
Notes: LAURA

## Slide 11: Tests (2/2)
IDLE
MANUAL MODE
EMERGENCY
MOVE
HOOK
Avoiding fixed obstacle
AVOIDANCE
Minimum distance of 15cm
Maximum 20 cm drift from trajectory
Identification of a fixed obstacle after 5s
Notes: ALEXIS + Laura au clic du diapo

## Slide 12: Part 3 : The analysis
Notes: ALEXIS / LEONIE

## Slide 13
Sprint evaluation
Avoiding fixed obstacle
Getting an obstacle position with LIDAR
Minimum distance of 15cm
Obstacle position +/- 5cm
Sending GPS coordinates
Maximum 10m one from another
Sending acknowledgement
Maximum 10 s after receiving the coordinates
Obstacle width
+/- 5 cm
Maximum 20 cm drift from trajectory
GPS coordinates +/- 0,0001 °
(≈ 50cm)
Identification of a fixed obstacle after 5s
Get the cars direction with the IMU
Notes: LEONIE
13

## Slide 14: Time Schedule
Get obstacle width and position with the Lidar
Detecting and avoiding obstacles
Higher Priority
Time
10/01
13/12
Lower Priority
Léonie
Alexis
Martin
20/12
Implement the avoiding trajectory
27/12
03/01
Samantha
Imane
Laura
8
13
Detecting small or big moving obstacles
3
Communicating with the damaged car
Send GPS coordinates to the towing vehicle
Configurate the communication between the two cars (send ACK)
Get the GPS coordinates of the damaged car
3
3
3
Alexis
Samantha
Notes: LAURA

## Slide 15: Time Schedule
Get obstacle width and position with the Lidar
Detecting and avoiding obstacles
Higher Priority
Time
10/01
13/12
Lower Priority
20/12
Implement the avoiding trajectory
27/12
03/01
Laura
8
13
Detecting small or big moving obstacles
3
Communicating with the damaged car
Send GPS coordinates to the towing vehicle
Configurate the communication between the two cars (send ACK)
Get the GPS coordinates of the damaged car
3
3
3
Alexis
1
Get the GPS coordinates of the damaged car
Send GPS coordinates to the towing vehicle
1
ROS2 advantages
Notes: LAURA

## Slide 16: Time Schedule
Get obstacle width and position with the Lidar
Detecting and avoiding obstacles
Higher Priority
Time
10/01
13/12
Lower Priority
Léonie
Alexis
20/12
Implement the avoiding trajectory
27/12
03/01
8
13
Detecting small or big moving obstacles
3
Communicating with the damaged car
Send GPS coordinates to the towing vehicle
Configurate the communication between the two cars (send ACK)
Get the GPS coordinates of the damaged car
3
3
3
Samantha
Notes: LAURA

## Slide 17: Time Schedule
Get obstacle width and position with the Lidar
Detecting and avoiding obstacles
Higher Priority
Time
10/01
13/12
Lower Priority
20/12
Implement the avoiding trajectory
27/12
03/01
Samantha
8
13
Detecting small or big moving obstacles
3
Communicating with the damaged car
Send GPS coordinates to the towing vehicle
Configurate the communication between the two cars (send ACK)
Get the GPS coordinates of the damaged car
3
3
3
5
Timer implementation
Notes: LAURA

## Slide 18: Time Schedule
Get obstacle width and position with the Lidar
Detecting and avoiding obstacles
Higher Priority
Time
10/01
13/12
Lower Priority
Martin
20/12
Implement the avoiding trajectory
27/12
03/01
Imane
8
13
Detecting small or big moving obstacles
3
Communicating with the damaged car
Send GPS coordinates to the towing vehicle
Configurate the communication between the two cars (send ACK)
Get the GPS coordinates of the damaged car
3
3
3
Get obstacle width and position with the Lidar
Get the cars direction with the IMU
8
8
LiDAR problems
Notes: LAURA

## Slide 19
Velocity chart
Chart: Story Points
| Sprint 1 | Sprint 2 | Sprint 3 | Sprint 4 | Sprint 5
Commitment | 48 | 37 | 40 | 33
Work completed | 48 | 37 | 30 | 23
Work added | 0 | 0 | 0 | 8
Notes: LAURA
Ajouter « bonus »
Adapter au dernier sprint ( on a fait moins que prévu)
19

## Slide 20: Part 4 : The risks
Notes: LAURA / MARTIN

## Slide 21
FMECA
Notes: MARTIN
21

## Slide 22
Trajectory
fault tree
Notes: ALEXIS
22

## Slide 23
Obstacle
fault tree
Notes: ALEXIS
23

## Slide 24: Part 5 : The plan
Notes: ALEXIS/IMANE

## Slide 25: Next sprint
Reaching the damaged car
Higher Priority
Time
24/01
10/01
Lower Priority
Imane
Martin
Samantha
17/01
Laura
Léonie
Alexis
Identify the position/orientation relative to the damaged car with the IMU
3
Document the project
Fix the CAN to reduce risks
8
Avoiding the obstacles
Improve the avoiding trajectory and coming back to the initial position
5
Adapt the maneuver to the orientation
1
Complete the Web Page
Finalize the project Plan
3
3
Notes: IMANE
Pistes :
Voir AMDEC : mettre en idle la voiture si perte de conexión
On est d’Accord, on ne fait pas l’approche ?

## Slide 26
Demonstration
Towing the car on a straight line
Setting manoeuvre of alignment
Sending GPS coordinates and acknowledgement
Avoiding fixed obstacle
Lining up with the damaged vehicle
Detecting small obstacles
Notes: SAMANTHA
26

## Slide 27
Demonstration
Towing the car on a straight line
Setting manoeuvre of alignment
Sending GPS coordinates and acknowledgement
Avoiding fixed obstacle
Lining up with the damaged vehicle
Detecting small obstacles
Without U-turn
Notes: SAMANTHA
27

## Slide 28
Demonstration
Towing the car on a straight line
Setting manoeuvre of alignment
Sending GPS coordinates and acknowledgement
Avoiding fixed obstacle
Lining up with the damaged vehicle
Detecting small obstacles
With U-turn
Notes: SAMANTHA
28

## Slide 29
Tests
Towing the car on a straight line
Determine the maneuver of alignment to do
Sending GPS coordinates and acknowledgement
Avoiding fixed obstacle
Manoeuvring to line up with the damaged vehicle
Detecting a small obstacle
Maximum 10m of gap
Maximum 10 s after receiving the coordinates
GPS coordinates +/- 0,0001 °
(≈ 50cm)
Minimum distance of 15cm
Maximum 20 cm drift from trajectory
Identification of a fixed obstacle after 5s
Stops 75 cm +/- 5 cm away from obstacle
Stops in less than 5s
Obstacle smaller than
30 cm
Alignment of maximum 5 cm interval
Autonomous towing
Tow the damaged car on a minimum 2m straight line
Orientation +/- 20°
Choice of the maneuver in less than 10s
Notes: SAMANTHA
29

## Slide 30
Detecting and avoiding fixed obstacle
Communicating the GPS coordinates of the damaged car
New
To improve
Determine the cars orientations with the IMU
Use the cars orientations to choose the maneuver
CAN
Security
Notes: SAMANTHA ?

## Slide 31: Questions ?
Notes: SAMANTHA ?