## Slide 1: Tow Mater 5SIEC 2022-2023 / By Team Benny
The aim of this project is to tow a damaged vehicle with an autonomous vehicle. The goal is to make safety our priority! The vehicle has to approach the damaged vehicle slowly, taking into account its environment. It has to detect and avoid obstacles on its way towards the damaged vehicle. Then it should park and maneuver to reach the towing device of the damaged car.
DETECTING AND
AVOIDING OBSTACLES
MANEUVERING TO ALIGN WITH THE DAMAGED CAR
COMMUNICATING
POSITION AND DIRECTION OF THE DAMAGED CAR
TOWING THE
DAMAGED CAR
STUDENTS
Léonie Hatte - Imane El Khamlichi - Alexis Pierre Dit Lambert -Martin Cheliz - Samantha Gorrin-Ascanio - Laura Mendes
Git project
Analyse the environment with a LiDAR
Identify if an obstacle is fixed or not
Approximate the dimensions of an obstacle with Ultrasonic Sensors
Approximate the position of an obstacle with Ultrasonic Sensors
Keep a security distance with the obstacle
Choose the best avoidance trajectory
Align the cars with the Ultrasonic Sensors
Follow a predefined trajectory
Choose between two maneuvers
Compute the directions of the cars with the IMU
Get the GPS coordinates
Send the information to the towing car
Send an acknowledgement to the damaged car
Identify the damaged car
Tow the damaged car on a minimum 2 meters
Reverse toward the damaged car to hook it
THE PRODUCT AND ITS ARCHITECTURE
TUTORS
Sébastien Delautier - Didier Le Botlan
LIDAR
ULTRASONIC SENSORS
About us
CAMERA
Raspberry Pi 3
Nucléo
Jetson Nano
HOOK
THE TOWING CAR STATE MACHINE
Speed regulation of the wheels
MOTORS
THE TOWING CAR ARCHITECTURE
Jetson Nano – ROS 2 Humble (Docker)
Raspberry Pi 3 – ROS 2 Humble
Nucléo F103RB
Nucléo
L476RG
Ethernet
CAN
MOTORS
ULTRASONIC SENSORS
IMU
GPS
CAMERA
LIDAR
HOOK
lmendes@insa-toulouse.fr
: Harder tasks
: Favorite tasks
: To improve
REACHING THE DAMAGED CAR
OUR FEATURES
Calculate the route to the damaged car
Go next to the damaged car
FUTUR FEATURE
Inertial Measurement Unit measures a body's angular rate and orientation, using a combination of accelerometers, gyroscopes and magnetometers.
Robot Operating System is a set of software libraries and tools. It provides an operating system-like environment for robots.
LIght Detection and Ranging is a method for determining ranges by targeting a surface with a laser and measuring the time for the reflected light to return to the receiver.
IMU